TIMER DEVICE
Author : Neha Karanjkar
March 2016

1. Addresses of Timer Control Register (32b) : 0x3100

2. Timer Control Word :
Timer_en
0
Timer_max_count
31:1

3. Timer Period : The period of the timer (delay between enabling a timer and the assrtion of the interrupt ) is given by :
Timer period = Timer_max_count/TIMER_TICK_REAL_FREQUENCY

The parameters TIMER_TICK_REAL_FREQUENCY, and TIMER_TICK_VIRTUAL_FREQUENCY are defined in Ajit_Hardware_Configuration.h.

4. Timer State Transitions :
The timer operates only in one-shot mode. It can be in one of following states:
- TIMER_DISABLED :The timer is in disabled state upon reset, and its interrupt output value is 0. When the cpu writes a control word with bit[0]=1, the count value is cleared and the timer moves to TIMER_ENABLED state.
- TIMER_ENABLED : When enabled, the timer keeps counting the number of ticks produced by a periodic tick source. The interrupt output is 0. When the count reaches "max_count",	interrupt output is asserted , count is cleared and the timer moves to TIMER_INTERRUPTING state.
- TIMER_INTERRUPTING : The timer stops counting, and the interrupt output remains high, until the cpu explicitly disables the timer by writing bit[0]=0 into the control word register.

TIMER_DISABLED
TIMER_ENABLED
TIMER_INTERRUPTING
RESET

Timer_en == 0 /
count = 0
INT = 0
tick,
count >= Timer_max_count /
count = 0
INT = 1

Timer_en == 1 /
count = 0
INT = 0

tick,
count<Timer_max_count /
count =count+1

Timer_en == 0 /
count = 0
INT = 0