INTERRUPT CONTROLLER DEVICE
Author : Neha Karanjkar
March 2016

1. Addresses of the INterrupt Controller (IRC) Control Register (32b) : 0x3000

IRC_en
0
Unused
31:1
2. IRC Control Word :

4. IRC State Transitions :

IRC_DISABLED
IRC_ENABLED
IRC_INTERRUPTING
RESET

IRC_en == 0 /
INT = 0
Interrupt signal received from device/
INT = Interrupt number of highest
priority interrupting source

IRC_en == 1 /
INT = 0

No external interrupt /
INT=0

IRC_en == 0 /
INT = 0