SERIAL DEVICE
Author : Neha Karanjkar
March 2016

1. Register Addresses
- Control Register (32b) : 0x3200
- Tx Register (8b) : 0x3210
- Rx Register (8b) : 0x3220

Tx_en
0
Rx_en
1
Rx_int_en
2
Tx_full
3
Rx_full
4
unused
31-5
2. Control Word :

3. Tx State Transitions :

TX_DISABLED
TX_ENABLED
TX_TRANSMITTING

RESET

Tx_en == 1 / Tx_full=0
Tx_en == 0
Write to Tx reg /
 Tx_full = 1
Tx finished transmitting /
 Tx_full = 0

4. Rx State Transitions :

RX_DISABLED
RX_ENABLED
RX_DATA_RECEIVED

RESET

Rx_en == 1 / Rx_full=0
Data received on Rx pin /
Rx_full = 1
INT = Rx_int_en
Rx register read by cpu /
Rx_full = 0
INT = 0

Rx_en == 0/
Rx_full = 0
INT = 0